# F/V “CAROLINE GLACIAL”

# - 50 m Longliner

N-5582 Ølensvåg, Norway

Tel: (+47) 53 77 50 00 – Fax: (+47) 53 77 50 01

Webadress: www.westcon.no

E-mail: westcon@westcon.no

## Principal particulars

Length o.a.:	49,99 m

Length p.p:	43,60 m

Breadth mid:	10,70 m

Depth to 1st deck:	9,90 m

Depth to 2nd deck:	7,50 m

Depth to 3rd deck:	5,00 m

Gross tonnage:	1139 Brt.

Accommodation:	41 men + hospital

Freezing hold capacity:	580 m3

Bait hold:	53 m3

Fuel oil capacity:	386 m3

Fresh water capacity:	24 m3

Speed:	14 knots

Class:	DnV + 1A1 Fishing vessel, ICE C

### Main Engine

Make:	Caterpillar

Type:	3606 TA

Power: 	2360 BHP/900 RPM

Gear/Propulsion line:	Volda ACG 627450

#### Electronical equipment

Radar A:	Furuno FR2110 ARPA

Radar B:	Furuno FR7111

Chartplotter:	Maxsea

Echosounder A:	Simrad ES500

Echo sounder B:	Simrad EQ50

Satcom system:	1 x Aritsu RS402A Inmacsat B

Main radio system:	Furuno FS1502

Watch receiver:	Sailor R 501

Gyro:	Robertson RGC11

Autopilot system: 	Robertson AP45MKII

GPS: 	2 x Furuno GP50MKII

VHF:	3 x Shipmate RS8400

Handheld VHF:	2 x ICOM

Weather fax:	Navtex receiver

Monitoring system:	4 x Sony Colour

Intercom System:	Vingtor Marine

Loudhailer:	Rayton RAY430

### Fish processing equipment

Freezing plant type:	Teknotherm

Freezing capacity:	30 t / 24 h

Fish factory:	P. E. Bjørdal AS

Temperature in hold:	-30(C

### Special equipment

Deck Cranes:	Karm SWL 2 t / 12 m

Karm SWL 1,5 t / 10 m

Autoline system:	Mustad 40.000 hooks

Fishing winch:	Westcon SWL 1 tonnes

Anchor winch:	Karm

Capstan:	Karm 2 tonnes

Fresh water generator:	Alfa Laval 12 t / 24 h

Fuel oil separator:	Alfa Laval

Air compressors:	Sperre HLF 2/77

Machine room pumps:	Allweiler Norge

Ventilation:	Nyborg

Air condition:	Covent CVCE2

Engine room CO2  plant:	Alf Lea

MOB boat:	DSB-kopas

Life rafts:	DSB 4 x 20 men

Navigation Lights: 	Tranberg

V E S S E L   I N F O R M A T I O N

50 M  LONGLINER

F/V CAROLINE GLACIAL

Delivered in 1997 by West Contractors AS, Ølensvåg, Norway as yard no. 12 for owner Glacial Shipping SA. The longliners are built for worldwide deep-sea fishing and are equipped with an extensive fish-processing factory.

N-5582 Ølensvåg, Norway

Tel: (+47) 53 77 50 00 – Fax: (+47) 53 77 50 01

Webadress: www.westcon.no

E-mail: westcon@westcon.no